## Slide 1
2023. 12. 06
SMEET LAB
Reducing the chattering problem in Sliding Mode Control (SMC) by using a Deep Neural Network (DNN) in torque vectoring

## Slide 2: Sliding Mode Control(SMC)
What is Sliding Model Control
  SMC is a nonlinear control approach which use relay as the basic control element
  The main purpose of SMC is to ensure system stability and robustness against uncertainties and external disturbances

## Slide 3: Sliding Mode Control(SMC)
Advantages of SMC
  Robustness
  System stability
  Simplicity and Ease of Implementation
  Nonlinear Control
Disadvantages of SMC
  Chattering

## Slide 4: Sliding Mode Control(SMC)
Example of the First order SMC
  Proportional control : u =-k(x-x_desired), SMC = u=-Ksing(x-x_desired) ; K is gain

## Slide 5: Sliding Mode Control(SMC)
Example of the First order SMC
  +d(disturbance)
  disturbance d = 0.5*sin(5t)

## Slide 6: Other Modern Control
Model predictive Control (MPC)
  Purpose : MPC uses a model of the process to predict the future behavior of the system. It optimizes control actions at each step based on a set of constraints and a cost function over a future prediction horizon
  Advantage : can handle multi-variable control problem, Flexible in adapting to changing system condition
  Disadvantage : Performance heavily relies on the accuracy of the model, and requires significant computational resources

## Slide 7: Other Modern Control
Linear Quadratic Regulator (LQR) Control
  Purpose: LQ control is aimed at minimizing a quadratic cost function, which typically includes terms for error and control effort. It is used mainly for linear systems.
  Advantage : Efficient for linear system, Easy to make
  Disadvantage : Linear system only, not robust

## Slide 8: Torque Vectoring
What is Torque Vectoring
  Torque Vectoring is distributing power individually to make extra yaw moment
  This extra momentum improve handling, stability and performance

## Slide 9: Torque Vectoring
Vehicle yaw momentum equation
  - -
  Control Value :
  unknown value :

## Slide 10: Torque Vectoring
Why SMC
  We have a dynamic model but due to non-linearity of tires, we can not get most the forces between the ground and tire. And This makes disturbance
  MPC may be accurate for this model, but it requires high computer power and time
  LQ is not Robust Control

## Slide 11: Torque Vectoring
Problem of SMC Chattering
  Causes of Chattering
    Finite of Function Frequency
    System Nonlinearities
    Model Uncertainties
    Actuator Limitation

## Slide 12: Torque Vectoring
Method for Chattering
  Boundary Layer
  Observer-based
  Regular form
  Disturbance rejection
Continuous
Estimate Disturbance using result
Discard disturbance using integration

## Slide 13: Torque Vectoring
Main purpose of my research
  Collect the data from the simulator and find the disturbance value to reduce gain value to address the chattering problem using a DNN
  Disturbance value is unknown value and differences with real and virtual
  It is not a definite output, it will be only disturbance or Gain too

## Slide 14: Torque Vectoring
Research plan
  Find the relation with variables and disturbance for select input data
  Make DNN model as small as possible for MCU
  The metrics for the model is the improvement of chattering problem
  Experiment real world (if I can)
  More advance DNN model added (if MCU can) because just DNN is not good at outlier

## Slide 15: References
V. Utkin, J. Guldner, and J. Shi, Sliding Mode Control in Electromechanical Systems. New York, NY, USA: Taylor & Francis, 1999.
Goggia, Tommaso, et al. "Integral sliding mode for the torque-vectoring control of fully electric vehicles: Theoretical design and experimental assessment." IEEE Transactions on Vehicular Technology 64.5 (2014): 1701-1715.

## Slide 16: Q&A

## Slide 17: THANK YOU!